## Slide 1
Tuning the Guts

## Slide 2: Outline
Configuration
IO stack
  SSDs and HDDs
  RAID controller
  Storage Area Network
  block layer and file system
  virtual storage
Multi-core
Network stack
Tuning
Tuning IO priorities
Tuning Virtual Storage
Tuning for maximum concurrency
Tuning for RAM locality
The priority inversion problem
Transferring large files
How to throw hardware at a problem?

## Slide 3: IO Architecture
RAID controller
PCI
Southbridge
Chipset
[z68]
SSD
SSD
SSD
HDD
HDD
PCI Express
SSD
SSD
SATA ports
Processor
[core i7]
Memory bus
RAM
LOOK UP: Smart Response Technology (SSD caching managed by z68)
16 GB/sec
2x21GB/sec
5 GB/sec
3 GB/sec
3 GB/sec

## Slide 4: IO Architecture
Exercise 3.1:
How many IO per second can a core i7 processor issue (assume that the core i7 performs at 180 GIPS and that it takes 500000 instructions per IO).
Exercise 3.2:
How many IO per second can your laptop CPU issue ( look up the MIPS
number associated to your processor).
Exercise 3.3:
Define the IO architecture for your laptop/server.

## Slide 5: Hard Drive (HDD)
Controller
read/write head
disk arm
tracks
platter
spindle
actuator
disk interface

## Slide 6: Solid State Drive (SSD)
Page program
Page program
Page program
Page program
Chip bound
Channel bound
Four parallel reads
Four parallel writes
Chip1
Chip2
Chip3
Chip4
Page
transfer
Page
read
Command
Chip bound
Read
Write
Logical address space
Scheduling & Mapping
Wear Leveling
Garbage collection
Read
Program
Erase
Chip
Chip
Chip
…
Chip
Chip
Chip
…
Chip
Chip
Chip
…
Chip
Chip
Chip
…
Flash memory array
Channels
Physical address space
Example on a disk with 1 channel and 4 chips

## Slide 7: RAID Controller
CPU
RAM
PCI bridge
Host Bus Adapter
Caching
  Write-back / write-through
Logical disk organization
  JBOD
  RAID
Batteries

## Slide 8: RAID
Redundant Array of Inexpensive Disks
RAID 0: Striping [n disks]
RAID 1: Mirroring [2 disks]
RAID 10: Each stripe is mirrored [2n disks]
RAID 5: Floating parity [3+ disks]
Exercise 3.4:
A – What is the advantage of striping over magnetic disks?
B- what is the advantage of striping over SSDs?

## Slide 9: Storage Area Network (SAN)
“A storage area network is one or more devices communicating via a serial SCSI protocol (such as FC, SAS or iSCSI).” Using SANs and NAS, W. Preston, O’Reilly
SAN Topologies
  Point-to-point
  Bus
    Synchronous (Parallel SCSI, ATA)
    CSMA (Gb Ethernet)
  Arbitrated Loop (FC)
  Fabric (FC)

## Slide 10: Case: TPC-C Top Performer (01/13)
Redo Log Configuration
Source: http://www.tpc.org/tpcc/results/tpcc_result_detail.asp?id=110120201
Total system cost | 30,528,863 USD
Performance | 30,249,688 tpmC
Total #processors | 108
Total #cores | 1728
Total storage | 1,76 PB
Total #users | 24,300,000
LOOK UP: TPC-C OLTP Benchmark

## Slide 11: IO Stack
DBMS
DBMS IOs:
Asynchronous IO
Direct IO

## Slide 12: Block Device Interface
Memory Abstraction:
@content <- read(LBA)
write(LBA, @content)
Block device specific driver
B0
B1
B2
B3
B4
B5
B6
B7
B8
B9
…
Bi
Bi+1
Linear Space of Logical Block Addresses (LBA)

## Slide 13: Performance Contract
HDD
  The block device abstraction hides a lot of complexity while providing a simple performance contract:
    Sequential IOs are orders of magnitude faster than random IOs
    Contiguity in the logical space favors sequential Ios
SSD
  No intrinsic performance contract
  A few invariants:
    No need to avoid random IOs
    Applications should avoid writes smaller than a flash page
    Applications should fill up the device IO queues (but not overflow them) so that the SSD can leverage its internal parallelism

## Slide 14: Virtual Storage
No Host Caching.
  The database system expects that the IO it submits are transferred to disk as directly as possible. It is thus critical to disable file system caching on the host for the IOs submitted by the virtual machine.
Hardware supported IO Virtualization.
  A range of modern CPUs incorporate components that speed up access to IO devices through direct memory access and interrupt remapping (i.e., Intel’s VT-d and AMD’s AMD-vi)). This should be activated.
Statically allocated disk space
  Static allocation avoids overhead when the database grows and favors contiguity in the logical address space (good for HDD).

## Slide 15: Processor Virtualization
Source: Principles of Computer System Design, Kaashoek and Saltzer.

## Slide 16: Dealing with Multi-Core
Source: http://pic.dhe.ibm.com/infocenter/db2luw/v9r7/topic/com.ibm.db2.luw.admin.perf.doc/doc/00003525.gif
SMP: Symmetric Multiprocessor
LOOK UP: Understanding NUMA
NUMA: Non-Uniform Memory Access

## Slide 17: Dealing with Multi-Core
LOOK UP: SW for shared multi-core, Interrupts and IRQ tuning
CPU
L1 cache
Core 0
CPU
L1 cache
Core 1
L2 Cache
Socket 0
CPU
L1 cache
Core 0
CPU
L1 cache
Core 1
L2 Cache
Socket 0
System Bus
IO, NIC Interrupts
RAM
Cache locality is king:
Processor affinity
Interrupt affinity
Spinning vs. blocking

## Slide 18: Network Stack
LOOK UP: Linux Network Stack
DBMS
(host, port)

## Slide 19: DNS Servers
Source: Principles of Computer System Design, Kaashoek and Saltzer.

## Slide 20: Tuning the Guts
RAID levels
Controller cache
Partitioning
Priorities
Number of DBMS threads
Processor/interrupt affinity
Throwing hardware at a problem

## Slide 21: RAID Levels
Log File
  RAID 1 is appropriate
    Fault tolerance with high write throughput. Writes are synchronous and sequential. No benefits in striping.
Temporary Files
  RAID 0 is appropriate
  No fault tolerance. High throughput.
Data and Index Files
  RAID 5 is best suited for read intensive apps.
  RAID 10 is best suited for write intensive apps.

## Slide 22: Controller Cache
Read-ahead:
  Prefetching at the disk controller level.
  No information on access pattern.
  Not recommended.
Write-back vs. write through:
  Write back: transfer terminated as soon as data is written to cache.
    Batteries to guarantee write back in case of power failure
    Fast cache flushing is a priority
  Write through: transfer terminated as soon as data is written to disk.

## Slide 23: Partitioning
There is parallelism (i) across servers, and (ii) within a server both at the CPU level and throughout the IO stack.
To leverage this parallelism
  Rely on multiple instances/multiple partitions per instance
    A single database is split across several instances. Different partitions can be allocated to different CPUs (partition servers) / Disks (partition).
    Problem#1: How to control overall resource usage across instances/partitions?
      Fix: static mapping vs. Instance caging
  Control the number/priority of threads spawned by a DBMS instance
    Problem#2: How to manage priorities?
    Problem#3: How to map threads onto the available cores
      Fix: processor/interrupt affinity

## Slide 24: Instance Caging
Allocating a number of CPU (core) or a percentage of the available IO bandwidth to a given DBMS Instance
Two policies:
  Partitioning: the total number of CPUs is partitioned across all instances
  Over-provisioning: more than the total number of CPUs is allocated to all instances
LOOK UP: Instance Caging
# Cores
Instance A
(2 CPU)
Instance B
(2 CPU)
Instance C
(1 CPU)
Instance D
(1 CPU)
Max #core
Partitioning
Over-provisioning
Instance A
(2 CPU)
Instance B
(3 CPU)
Instance C
(2 CPU)
Instance C
(1 CPU)

## Slide 25: Number of DBMS Threads
Given the DBMS process architecture
  How many threads should be defined for
    Query agents (max per query, max per instance)
      Multiprogramming level (see tuning the writes and index tuning)
    Log flusher
      See tuning the writes
    Page cleaners
      See tuning the writes
    Prefetcher
      See index tuning
    Deadlock detection
      See lock tuning
Fix the number of DBMS threads based on the number of cores available at HW/VM level
    Partitioning vs. Over-provisioning
    Provisioning for monitoring, back-up, expensive stored procedures/UDF

## Slide 26: Priorities
Mainframe DBMS allow to configure thread priority as well as IO priority
  Threads associated to synchronous IOs (writes to the log, page cleaning under memory pressure, query agent reads) should have higher priorities than threads associated to asynchronous IOs (prefetching, page cleaner with no memory pressure) – see tuning the writes and index tuning
  Synchronous IOs should have higher priority than asynchronous IOs.

## Slide 27: The Priority Inversion Problem
lock X
request X
Priority #1
T3
T1
T2
Priority #2
Priority #3
running
waiting
Transaction states
Three transactions: T1, T2, T3 in priority order (high to low)
  T3 obtains lock on x and is preempted
  T1 blocks on x lock, so is descheduled
  T2 does not access x and runs for a long time
Net effect: T1 waits for T2
Solution:
  No thread priority
  Priority inheritance

## Slide 28: Processor/Interrupt Affinity
Mapping of thread context or interrupt to a given core
  Allows cache line sharing between application threads or between application thread and interrupt (or even RAM sharing in NUMA)
  Avoid dispatch of all IO interrupts to core 0 (which then dispatches software interrupts to the other cores)
  Should be combined with VM options
  Specially important in NUMA context
  Affinity policy set at OS level or DBMS level?
LOOK UP: Linux CPU tuning

## Slide 29: Processor/Interrupt Affinity
IOs should complete on the core that issued them
  I/O affinity in SQL server
  Log writers distributed across all NUMA nodes
Locking of a shared data structure across cores, and specially across NUMA nodes
  Avoid multiprogramming for query agents that modify data
  Query agents should be on the same NUMA node
DBMS have pre-set NUMA affinity policies
LOOK UP: Oracle and NUMA, SQL Server and NUMA

## Slide 30: Transferring large files (with TCP)
With the advent of compute cloud, it is often necessary to transfer large files over the network when loading a database.
To speed up the transfer of large files:
  Increase the s ize of the TCP buffers
  Increase the socket buffer size (Linux)
  Set up TCP large windows (and timestamp)
  Rely on selective acks
LOOK UP: TCP Tuning

## Slide 31: Throwing hardware at a problem
More Memory
  Increase buffer size without increasing paging
More Disks
  Log on separate disk
  Mirror frequently read file
  Partition large files
More Processors
  Off-load non-database applications onto other CPUs
  Off-load data mining applications to old database copy
  Increase throughput to shared data
    Shared memory or shared disk architecture